## Slide 1: Coherent detection: transmitted vs real LO
Transmitted LO: both quantum signal and LO provided by the same laser.
  Phase alignment relatively simple and noise free (at least in principle).
  Vulnerabilities due to manipulation of LO in the channel by Eve.
  Noise due to scattering in the channel from the strong LO.
Opt. Lett. 40, 3695 (2015); Phys. Rev. X 5, 041009 (2015);
Phys. Rev. X 5, 041010 (2015); arXiv:1605.03642
Real LO: only signal on quantum channel, Bob uses an independent laser for LO.
  Alignment to a common time & phase reference becomes challenging.
  Two lasers = higher cost + characterization effort.