## Slide 1
Investigating feasibility of broadband continuous variable quantum key distribution in telecom fibers with local local oscillator
N. Jain,1 C.S. Jacobsen,1 D. Solar Nikolic,1 A. Kordts,1 C. Lupo,2
R. Grigoryan,1 T. Pedersen,3 S. Pirandola,2,4 T. Gehring,1 and U.L. Andersen1
Introduction
Current setup and component characterization
Results
1Department of Physics, Fysikvej 309, Technical University of Denmark, 2800 Kongens Lyngby, Denmark
2York Centre for Quantum Technologies (YCQT), University of York, York YO10 5GH, United Kingdom
3Cryptomathic A/S, Jaegergardsgale 118, 8000 Aarhus, Denmark
4Department of Computer Science, University of York, York YO10 5GH, United Kingdom
References
[1]
The use of continuous variable (CV) quantum information carriers, instead of qubits, constitutes a powerful alternative approach for quantum key distribution (QKD). In contrast to other approaches, CV-QKD implementations have the advantage that they rely on standard telecommunication technology such as lasers, fibers, and in particular, coherent detection techniques.
The best understood CV-QKD protocols, in terms of security proofs and practical implementations, are one-way protocols using coherent states with Gaussian modulation. These protocols are proven to be secure against collective Gaussian attacks in the finite size regime. Here, we present the progress in realization of our CVQKD scheme and the challenges faced in adapting the security proof to real-world scenarios.
Design dilemmas: transmitted LO vs. local LO & homodyne vs. heterodyne
CV-QKD systems employ receivers performing phase-sensitive detection using a local oscillator (LO) whose phase drift w.r.t. the sent quantum signal (qSig) must be precisely controlled/estimated. Until recently, all known CV-QKD implementations used the transmitted LO (TLO) design. A novel local LO (LLO) design obviates some limitations of the TLO design but brings in some new challenges.
Stable relative phase between qSig and LO at the receiver
Vulnerable to LO intensity/wavelength manipulation on quantum channel
LO intensity limitation at receiver due to propagation losses and non-linear effects
Difficulty in estimating relative phase between qSig and LO; complicated phase correction using reference signals need to be employed
LO can be fully trusted, security loopholes closed
No limitation on the local LO intensity
Balanced detection involves interfering the sent signal with the LO on a 50/50 splitter. Depending on the frequency detuning ΩΔ between the signal and LO, one performs homodyne (ΩΔ = 0) or heterodyne detection (ΩΔ ≠ 0). Heterodyning allows recovering the full info about Sig but with a 3dB penalty.
A general expression for the output current of balanced receiver:
AM
PM
laser
AWG/
FPGA board
VATT
PMF
SMF
real LO
laser
VATT
heterodyne detection
(ωb ≠ 0)
(Demodulation &)
Oscilloscope/ADC
-
NKT Photonics X15 and E15 lasers
Broadband coding may require a thorough
pre-characterization of the modulators and
detector response (transfer function) in the
frequency band of interest.
Data processing performed offline in MATLAB with digital PLL for recovering the modulated data
The current setup employs amplitude and phase modulators which create double sideband
The future setup will use single-sideband modulation for better spectral efficiency and closing potential security loopholes
Introduction of pilot signals for clock recovery, multiplexed in time with the quantum signal
Carrier synchronization on receiver side
Replacing AWG and oscilloscope with FPGA DAC/ADC suite for online signal generation and recovery
Future steps
Security analysis
PMF
SMF
IQmod
laser
FPGA
(RF mod)
VATT
QRNG
dynamic polarization
controller
½
laser
VATT
ADC, clock recovery,
demodulation,
reconstruction etc.
ADC, clock recovery,
demodulation,
reconstruction etc.
heterodyne detection
(ωb ≠ 0)
A composable security proof for the most general attacks in Gaussian CV-QKD systems is still an open problem
It is proved that the system is secure against collective attacks for continuous Gaussian modulation of coherent states; this is very important result since general coherent attacks will be possible only with very advanced quantum adversary in, what is believed, not so near future
The main focus of our theoretical research is estimating final key length taking into account finite block length and inevitable discretization of Gaussian modulation
Current security proof provides an expression for secret key length:
EQUATION FROM COSMO
Assuming small modulation depths, quadrature DC bias on AM, and negligible phase noise and drifts in the setup:
Transmitted LO
Local LO